Signaling
        =========

Signaling is a mechanism to send the digital data in form of bits as voltage pulses.

There are two types of signaling generally used in digital electronics :
1.) Single-ended signaling
2.) Differential signaling.

1.) Single-ended signaling:
This type of signaling is generally used in half-duplex method or other similar
       methods where one signal requires only 1 wire to transmit bits, and 1 wire acts as
common ground if multiple signals has to be transmitted.
So for exchanging 10 different signals, one need a cable with 11 wires, 10 for
voltage pulses and 1 for common ground with whose relative the pulse potential
would be.

A probable problem with single-ended signaling is that noise can cause signal
 distortion, in order to neglect the signal distortion/noise, the magnitude of voltage
pulse must be significantly higher than the noise voltage, thus requires higher power
 for transmission, Single-ended signaling typically requires signal voltage to be ~5V	or more or the design must be using some sort of noise cancellation mechanism in
order to reduce higher power consumption.

2.) Differential signaling:
This type of signaling is used in CAN networks and other requirement specific
 circuits, this signaling requires two wires to transmit a single signal along with a
common ground.
At the receiver's end, their must be a differential amplifier to take the difference of
 the potential between two wires.
If one need to transmit 10 signals, 21 wires will be required, 20 for signals, 1 for
common ground.

But how does the differential signaling works ???

The wires are assigned names as D+ and D- , both wires carries same potential but of
 opposite polarity at each instant of time when the circuit is in operable state.

logical 1 is represented when D+ is at higher potential than D- , say D+ at 2.5V and	D- at -2.5V.

logical 0 is represented when D- is at higher potential than D+ , say D- at 2.5V and	D+ at -2.5V.

 note that at every time instant when the device is in operable state, both wires are at	equal but opposite potential.

Advantages of differential signaling :
* Common mode rejection :
Any piece of small signal which is common on both the wires	will be cancelled out by the differential amplifier, say a noise is
 induced in both the D+ and D- signals, then at the receiver's
 end, when the differential amplifier performs the operation :	(D+) - (D-) , the common noise signal will be cancelled giving
 it name as 'Common mode rejection'.
* Lower power consumption :
In case of Single-ended signaling, in order to overcome the	noise impact on original signal, the voltage level of bit
 carrying pulses must be high in order to correctly interpret the
 potential, but in case of differential signaling, the noise
 cancellation is handled by differential amplifier at receiver's
 end, thus we don’t need to worry about noise, then why should
 we even use higher voltage levels for pulse/bit transfer ?,
 definitely not, the small pulse voltages are used to transmit bits	over the channel, and also the signal gets amplified at
 receiver's end as well, thus signal potential must only be large
 enough that differential amplifier can significantly work with	it.